## Slide 1: Rethinking NoCs for Spatial Neural Network Accelerators
Oct 20, 2017
Georgia Institute of Technology
Synergy Lab (http://synergy.ece.gatech.edu)
Hyoukjun Kwon, Ananda Samajdar, and Tushar Krishna
NOCS 2017

## Slide 2: Emergence of DNN Accelerators
Emerging DNN applications

## Slide 3: Emergence of DNN Accelerators
Convolutional Neural Network (CNN)
Conv.
Layer
Conv.
Layer
...
Conv.
Layer
Pool.
Layer
FC
Layer
“Palace”
Intermediate features
Convolutional Layers
(Feature Extraction)
Summarize features
Notes: Features -> could be edges, etc.

## Slide 4: Emergence of DNN Accelerators
Sliding window operation over input featuremaps
Computation in Convolutional Layers
Image source: Y. Chen et al., Eyeriss: A Spatial Architecture for Energy-Efficient Dataflow for Convolutional Neural Networks, ISCA 2016
Notes: Explain from images -> filters -> (convolving them) output

## Slide 5: Emergence of DNN Accelerators
for(n=0; n<N; n++) { // Input feature maps (IFMaps)
for(m=0; m<M; m++) { // Weight Filters
for(c=0; c<C; c++) { // IFMap/Weight Channels
for(y=0; y<H; y++) { // Input feature map row
for(x=0; x<H; x++) { // Input feature map column
for(j=0; j<R; j++) { // Weight filter row
for(i=0; i<R; i++) { // Weight filter column
O[n][m][x][y] += W[m][c][i][j] * I[n][c][y][x]}}}}}}}
Multiplication
Accumulation
Massive Parallelism in Convolutional Layers

## Slide 6: Emergence of DNN Accelerators
Spatial DNN Accelerator ASIC Architecture
168 PEs
256 PEs (16 in each tile)
Dadiannao (MICRO 2014)
Eyeriss (ISSCC 2016)
*PE: processing element
Notes: General purpose is not as efficient as DNN accelerators (not good for exracting the paralleims)

## Slide 7: Emergence of DNN Accelerators
Global Memory
(GBM)
NoC
PE
PE
PE
...
PE
PE
PE
...
PE
PE
PE
...
Multi-Bus: Eyeriss
Mesh: Diannao, Dadiannao
Crossbar+Mesh: TrueNorth
Spatial DNN Accelerator ASIC Architecture
Spatial processing over PEs
DRAM
PE Array
Notes: Why do we need a NoC? => Support different traffic patterns dependning on the DNN that is mapped. (If we have only one to support, a special structure wiil be sufficient )

## Slide 8: Challenges with Traditional NoCs
Mesh
Crossbar Switch
Bus
Throughput
PE
Eyeriss PE
Size of squares of NoC: Total area divided by the number of PEs (256 PEs)
Relative Area Overhead Compared to Tiny PEs
Notes: Correspondingly power is also huge
Mesh/crossbar are good for CMPs that the cores are large
Let’s look at meshes and buses

## Slide 9: Challenges with Traditional NoCs
Bus provides low bandwidth for DNN traffic
Bandwidth
Alexnet Conv. layer
Simulation Results (RS)
Serialized broad-/multi-casting
Bandwidth bottleneck at top level
Notes: Details about the simulation will be explained later
Compare bus vs mesh
Latency -> Runtime
No clear winner
More PEs -> should lower latency

## Slide 10: Challenges with Traditional NoCs
Dataflow Style Processing over Spatial PEs
Eyeriss
Systolic Array (TPU)
...
...
PE
PE
PE
PE
PE
PE
PE
PE
PE
...
...
PE
PE
PE
PE
PE
PE
PE
PE
PE
Traffic is different from that of CMPs and MPSoCs
No way to hide the latency

## Slide 11: Challenges with Traditional NoCs
Unique Traffic Patterns
CMPs
Core
Core
Core
Core
Core
GPU
Sen
sor
Comm
MPSoCs
GBM
NoC
PE
PE
PE
PE
DNN Accelerators
Dynamic
all-to-all traffic
Static fixed traffic
?

## Slide 12: Traffic Patterns in DNN Accelerators
Scatter
One-to-All
GBM
NoC
PE
PE
PE
PE
One-to-Many
GBM
NoC
PE
PE
PE
PE
E.g., filter weight and/or input feature map distribution

## Slide 13: Traffic Patterns in DNN Accelerators
Gather
All-to-one
GBM
NoC
PE
PE
PE
PE
Many-to-one
GBM
NoC
PE
PE
PE
PE
E.g., partial sum gathering

## Slide 14: Traffic Patterns in DNN Accelerators
Local
Many one-to-one
GBM
NoC
PE
PE
PE
PE
Key optimization to remove traffic between GBM and PE array and maximize data reuse in the PE array
e.g., psum accumulation

## Slide 15: Why Not Traditional NoCs
Unique Traffic Patterns
CMPs
Core
Core
Core
Core
Core
GPU
Sen
sor
Comm
MPSoCs
GBM
NoC
PE
PE
PE
PE
DNN Accelerators
Scatter
Gather
Local
Dynamic
all-to-all traffic
Static fixed traffic

## Slide 16: Requirements for NoCs in DNN Accelerators
Requirements
  High throughput: Many PEs
  Area/power efficiency: Tiny PEs
  Low latency: No latency hiding
  Reconfigurability: Diverse neural network dimensions
Optimization Opportunity
  Three traffic patterns: Specialization for each traffic

## Slide 17: Outline
Motivations
Microswitch Network
  Topology
  Routing
  Microswitch
  Network Reconfiguration
  Flow control
Evaluations
  Latency (throughput)
  Area
  Power
  Energy
Conclusion

## Slide 18: Topology: Microswitch Network
Distribute communication to tiny switches
Lv 0
Lv 1
Lv 2
Lv 3
Top Switch
Middle Switch
Bottom Switch
Notes: REmove Other GBM links

## Slide 19: Routing: Scatter Traffic
Tree-based broad/multicasting

## Slide 20: Routing: Gather Traffic
Multiple pipelined linear network
Bandwidth bound to GBM write bandwidth
Notes: Mention arbiter

## Slide 21: Routing: Local Traffic
Linear single-cycle multi-hop (SMART*) network
H. Kwon et al., OpenSMART: Single cycle-Multi-hop NoC Generator in BSV and Chisel, ISPASS 2017
T. Krishna et al., Breaking the On-Chip Latency Barrier Using SMART, HPCA 2013

## Slide 22: Microarchitecture: Microswitches
Notes: As spatial accelerators distribute computation over tiny PEs, we distribute communication over tiny switches

## Slide 23: Microswitches: Top Switch
Scatter Traffic
Gather Traffic
Local Traffic
Only required for switches connected with global buffer
Only required if a switch has multiple gather inputs
Notes: Red boxes: Only necessary to some of the switches

## Slide 24: Microswitches: Middle Switch
Scatter Traffic
Gather Traffic
Local Traffic
Only required for switches in the scatter tree
Notes: Red boxes: Only necessary to some of the switches

## Slide 25: Microswitches: Bottom Switch
Scatter Traffic
Gather Traffic
Local Traffic
Notes: Red boxes: Only necessary to some of the switches

## Slide 26: Topology: Microswitch Network
Lv 0
Lv 1
Lv 2
Lv 3
Top Switch
Middle Switch
Bottom Switch

## Slide 27: Outline
Motivations
Microswitch Network
  Topology
  Routing
  Microswitch
  Network Reconfiguration
  Flow control
Evaluations
  Latency (throughput)
  Area
  Power
  Energy
Conclusion

## Slide 28: Scatter Network Reconfiguration
Control Registers
En_Up
En_Down
Notes: Firstbit: Upper

## Slide 29: Scatter Network Reconfiguration
Reconfiguration logic
Recursively check destination PEs in upper/lower subtrees
En_Up
En_Down
Notes: Firstbit: Upper

## Slide 30: Scatter Netowrk Recofiguration
Reconfiguration logic

## Slide 31: Local Network: Linear SMART
Dynamic traffic control
Static traffic control
Supports multiple multi-hop local communication
H. Kwon et al., OpenSMART: Single cycle-Multi-hop NoC Generator in BSV and Chisel, ISPASS 2017
T. Krishna et al., Breaking the On-Chip Latency Barrier Using SMART, HPCA 2013
Notes: WHen does

## Slide 32: Reconfiguration Policy
Scatter Tree
  Coarse-grained: Epoch-by-epoch
  Fine-grained: Cycle-by-cycle for each data
Gather
  No reconfiguration (flow control-based)
Local
  Static: Compiler-based
  Dynamic: Traffic-based
* Accelerator Dependent
Notes: Pipelined We are just supporting all the possible dataflow

## Slide 33: Flow Control
Scatter Network
  On/Off flow control
Gather Network
  On/Off flow control between microswitches
Local Network
  Dynamic flow control: Global arbiter-based control
  Static flow control: SMART* flow control
* SMART flow control
Hyoukjun Kwon et al., OpenSMART: Single cycle-Multi-hop NoC Generator in BSV and Chisel, in ISPASS 2017
Tushar Krishna et al., Breaking the On-Chip Latency Barrier Using SMART, in HPCA 2013

## Slide 34: Flow Control
Why not credit-based flow control?
  Tiny microswitches: low latency for on/off signals delivery
  Reduce overhead of credit registers
Short distance
No Credit Registers

## Slide 35: Outline
Motivations
Microswitch Network
  Topology
  Microswitch
  Routing
  Network Reconfiguration
  Flow control
Evaluations
  Latency/throughput
  Area
  Power
  Energy
Conclusion

## Slide 36: Evaluation Environment
Target Neural Network | Alexnet
Implementation | RTL written in Bluespec System Verilog (BSV)
Accelerator Dataflow | Weight-Stationary (No local traffic) and Row-stationary (Exploit local traffic)*
Latency Measurement | RTL simulation over BSV implementation using Bluesim
Synthesis Tool | Synopsys Design Compiler
Standard Cell Library | NanGate 15nm PDK
Baseline NoCs | Bus, Tree, Crossbar, Mesh, and H-Mesh
PE Delay | 1 cycle
* Y. Chen et al., "Eyeriss: A Spatial Architecture for Energy-Efficient Dataflow for Convolutional Neural Networks," ISCA 2016

## Slide 37: Evaluations
Latency (Entire Alexnet Convolutional layers)
Microswitch reduces the latency by 61% compared to mesh
Notes: Most congested links?
Find the average link utliization

## Slide 38: Evaluations
Area
Microswitch NoC requires 16% area of mesh

## Slide 39: Evaluations
Power
Microswitch NoC only consumes 12% power of mesh
Notes: Go faster

## Slide 40: Evaluations
Energy
Buses always need to broadcast, even for unicast traffic
Microswitch NoC enables only necessary links

## Slide 41: Conclusion
Traditional NoCs are not optimal for traffic in spatial accelerators because such NoCs are tailored for random traffic in cache-coherence traffic in CMPs
Microswitch NoC is a scalable solution for four goals, latency, throughput, area, and energy, while traditional NoCs only achieve one of two of them
Microswitch NoC also provides reconfigurability so that it can support the dynamism across neural network layers

## Slide 42: Conclusion
Microswitch NoC is applicable to any spatial accelerator (e.g., cryptography, graph)
Microswitch NoC will be available as open source.
  Please sign up via this link
  http://synergy.ece.gatech.edu/tools/microswitch-noc/
  For general purpose NoC, openSMART is available http://synergy.ece.gatech.edu/tools/opensmart
Thank you!