## Slide 1: ASPLOS Lunch

## Slide 2: ASPLOS Lunch
Unused
seats
-Increases total lunch time
- More serving efforts
Narrow space between tables
Fixed table size

## Slide 3: DNN Accelerator
Underutilized
compute units
- Increased total runtime
- More energy
DNN Accelerator
Narrow interconnection
Inflexible compute unit design

## Slide 4: MAERI: Enabling Flexible Dataflow Mapping via Reconfigurable Interconnects
Mar 27, 2018
MAERI (http://synergy.ece.gatech.edu/tools/maeri/)
Synergy Lab (http://synergy.ece.gatech.edu)
Georgia Institute of Technology
Hyoukjun Kwon, Ananda Samajdar, and Tushar Krishna
ASPLOS 2018

## Slide 5: Deep Neural Network (DNN) Applications

## Slide 6: Convolutional Neural Network (CNN)
Conv.
Layer
Conv.
Layer
...
Conv.
Layer
Pool.
Layer
FC
Layer
“House”
Intermediate features
Convolutional Layers
(Feature Extraction)
Summarize features
Massive
Parallelization Opportunity

## Slide 7: Accelerating DNN Computation
GPUs
High Throughput
Energy Efficiency
Flexibility
Energy Efficiency
High Throughput
Inflexible Design
Specialized ASICs
Eyeriss (2016)
Dadiannao (2014)
...
Irregular Dataflow

## Slide 8: Sources of Irregular Dataflow
DNN Topologies
  Layer size / shape
  Layer types: Convolution / Pool / FC / LSTM
  New sub-structure: e.g., Inception in Googlenet
Dataflow Optimization
  Loop reordering
  Loop tiling
  Cross-layer mapping
Algorithmic Optimization
  Weight pruning: Sparse workload

## Slide 9: Accelerators for Each Irregular Dataflow
Sparse CNN: SCNN (2017), EIE(2016), ...
Cross-layer: Fused CNN (2016)
Dataflow: FlexFlow (2017), Eyeriss (2016), ...
LSTM: ESE (2017), ...
Can we have one architectural solution to rule them all?
...
Identify common computation/communication patterns across all of them
Notes: If we need one DNN acc in a chip -> we need something (LOTR meme)

## Slide 10: Outline
Motivation
DNN Compute & Communication
MAERI Approach
MAERI Architecture
Evaluation
Conclusion

## Slide 11: Background: Convolutional Layer in CNN
Compute weighted sum
Independent multiplication
Accumulation of multiplication results
Notes: First show CNN sliding window figure

## Slide 12: Regular Dataflow
Similar to dense matrix multiplication
Regular communication pattern between buffer and compute units
Notes: First show CNN sliding window figure

## Slide 13: Irregular Dataflow: Fused-Layer
Example: Cross-layer Mapping
Irregular number of weight/input pairs for each neuron
* M. Alwani et al., Fused-Layer CNN Accelerators, MICRO 2016
For simplicity, folded over row
For simplicity, folded over row

## Slide 14: Irregular Dataflow: Pruning
Example: Weight Pruning (Sparse Workload)
Irregular number of weight/input pairs for each neuron
Pruning
Notes: Removed edges -> color

## Slide 15: Underutilization from Irregular Neuron Size
Key Insight: Rigid Interconnect does not allow efficient mapping of irregular dataflows
Example: Weight Pruning (Sparse Workload)

## Slide 16: Take-aways
New optimizations
Irregular Neuron Size
Rigid Interconnection in Accelerators
Compute Resource
Underutilization
Reconfigurable Interconnection
Compute Resource
High Utilization

## Slide 17: Outline
Motivation
DNN Compute & Communication
MAERI Approach
MAERI Architecture
Evaluation
Conclusion

## Slide 18: Designing a Fully Flexible Accelerator
MultiplierPool
Adder
Pool
VN0
VN1
VN2
Virtual Neuron (VN): Temporary grouping of compute units for an output (neuron)
How to enable flexible grouping?
“MultAlloc(3); AddAlloc(2)”
Need to provide flexible connectivity among arbitrary compute units and buffer
NN figure showing 3 neurons highighted

## Slide 19: Naïve Approach: Fully-connected Design
Wire overhead = O(n2)
Need “specialization” in interconnection network
for traffic in DNN accelerators

## Slide 20: Traffic Patterns in DNN Accelerators*
PB
NoC
PE
PE
PE
PE
Distribution
PB
NoC
PE
PE
PE
PE
Collection
PB
NoC
PE
PE
PE
PE
* PB: Prefetch buffer (Global buffer)
* NoC: Network-on-Chip (Interconnection network)
* PE: Processing element (Compute units)
Local Forwarding
* H. Kwon et al., Rethinking NoCs for Spatial DNN Accelerators, NOCS 2017
e.g. weight distribution to PEs in weight-stationary accelerator
e.g. output collection in output-stationary accelerator
e.g. Input forwarding in row-stationary accelerator

## Slide 21: Practical Approach: Minimal Switches
2 x 2 switch
3 x 2 switch
One port for distribution
One port for local forwarding
Two ports for collection
Extra port for flexible mapping
Using these minimal switches...
How do we design a specialized connectivity (topology) allowing flexible mapping?

## Slide 22: Connectivity: Distribution of Weights/Inputs
Extra bandwidth
Features
Tree-based topology
  Supports multicasting for spatial data reuse
Extra bandwidth near the top
  Provides high bandwidth that enables multiple multicasting simultaneously

## Slide 23: Connectivity: Collection of Outputs
Extra bandwidth
Extra link
Extra link
enabled
red VN
Augmented Reduction Tree (ART)
Features
Extra links
  Supports non-blocking in-network reductions for arbitrary virtual neuron sizes
  Provides high compute unit utilization
Extra bandwidth near the root switch
  Provides high bandwidth that enables multiple reduction (accumulation) simultaneously

## Slide 24: Connectivity: Local Communication
Enables spatio-temporal date reuse

## Slide 25: Outline
Motivation
DNN Compute & Communication
MAERI Approach
MAERI Architecture
Evaluation
Conclusion

## Slide 26: Switch Microarchitecture
Light-weight structure

## Slide 27: MAERI DNN Accelerator
(VN Construction)

## Slide 28: MAERI DNN Accelerator: Features
Novel tree-based topology
  Provides near-non-blocking communication via reconfigurable links with high-bandwidth
  Support efficient irregular dataflow mapping
  Provides high utilization of compute units
Data reuse support
  Temporal: enabled via local buffers in mult. switches
  Spatial: enabled via multicasting in distribution tree
  Spatio-Temporal: enabled via forwarding links between multiplier switches

## Slide 29: MAERI DNN Accelerator: Features
Regular/Irregular Dataflow Support
  Dense convolution
  Sparse convolution
  Fully-connected layer
  LSTM
  Cross-layer fusion
  ...
Details in paper!

## Slide 30: Outline
Motivation
DNN Compute & Communication
MAERI Approach
MAERI Architecture
Evaluation
Conclusion

## Slide 31: Evaluation
Performance
  Dense workload: Convolution layer
  Irregular workload: Cross-layer workload
Impact of Interconnect
  Variable virtual neuron size
Overhead
  Area/power overhead (post-synthesis)

## Slide 32: Performance with Dense Workload
Baseline
8x8 Systolic Array
64-PE Row-stationary Accelerator
TPU-Style
Eyeriss-Style

## Slide 33: Performance with Dense Workload
Total Latency (Runtime)
* Normalized to ideal case (100% utilization, Infinite bandwidth)
In average, MAERI reduces runtime upto 65%, 42% in avg.
Foldings due to Large filter size(11x11, 5x5)
Notes: Compiler Opitimzation

## Slide 34: Evaluation
Performance
  Dense workload: Convolution layer
  Irregular workload: Cross-layer workload
Impact of the Interconnect
  Variable virtual neuron size
Overhead
  Area/power overhead (post-synthesis)

## Slide 35: Performance with Cross-layer Workload
Baseline
SCNN* Style, 64PEs
* A. Parashar et al., SCNN: An Accelerator for Compressed-sparse Convolutional Neural Networks, ISCA 2017

## Slide 36: Performance with Cross-layer Workload
Speed-up and Utilization
8-33% better utilization
23% speed-up in average
Fused Alexnet
MapA: C1+C2+C3
MapB: C2+C3+C4
MapC: C3+C4+C5
MapD: C1+C2+C3+C4
MapE: C2+C3+C4+C5

## Slide 37: Evaluation
Performance
  Dense workload: Convolution layer
  Irregular workload: Inter-layer workload
Impact of Interconnect
  Variable virtual neuron size
Overhead
  Area/power overhead (post-synthesis)

## Slide 38: Utilization with Various VN Size
Baseline
Base Tree Size = 16 (Increase tree size by 2 when mapped VN size is larger than current size)

## Slide 39: Utilization with Various VN Size
Workload: VGG-16 CONV6
Wide links
Augmented links
ART in MAERI
249% better utilization in average

## Slide 40: Evaluation
Performance
  Dense workload: Convolution layer
  Irregular workload: Inter-layer workload
Impact of Interconnect
  Variable virtual neuron size
Overhead
  Area/energy overhead (post-synthesis)

## Slide 41: Overhead Evaluation Environment
Technology: Synopsys 28nm
Implementation: Bluespec System Verilog
Designs
  Row-stationary (Eyeriss style)
  Systolic array (TPU style)
  MAERI
Comparison Method: Compute match
  All the designs have the same number of PEs as Eyeriss (168 PEs)

## Slide 42: Overhead: Area
With the same area as row-stationary, MAERI houses 2.33X more compute units
* With 168 PEs, post-synthesis number
Cost of
reconfigurability
Fully-addressable scratchpad

## Slide 43: Energy with Convolution Layers
MAERI reduces energy upto 57% and 28% in average compared to Row-Stationary (dense dataflow) and 7.1% in average compared to Systolic Array (sparse dataflow)
* Normalized to MAERI energy with Alexnet C1

## Slide 44: Outline
Motivation
DNN Compute & Communication
MAERI Approach
MAERI Architecture
Evaluation
Conclusion

## Slide 45: Conclusion
Diverse DNN dimensions and optimizations (sparsity, fused layer, etc.) introduce irregular dataflow in DNN accelerators
Most of DNN accelerators contain rigid interconnections that lead to under-utilization with irregular dataflow
MAERI provides reconfigurable non-blocking interconnect between compute units and sufficient bandwidth to support both regular and irregular dataflow
MAERI provided 8-458% better compute unit utilization across multiple dataflow mappings that results in 72.4% lower latency in average

## Slide 46: Announcement
Tutorial in ISCA 2018
Half-day tutorial on June 3 (morning)
T10: An Open Source Framework for Generating Modular DNN Accelerators supporting Flexible Dataflow
(http://synergy.ece.gatech.edu/tools/maeri/maeri_tutorial_isca2018/)
          Formal Dataflow analysis methodology
          MAERI RTL Release
          Deep-dive and Examples
Thank you!