## Slide 1: MAERI: An Open-source Framework for Generating DNN Accelerators with Flexible Dataflow Support
June 3, 2018
*Synergy Lab, Georgia Institute of Technology
** Architecture Research Group, NVIDIA
Hyoukjun Kwon*, Michael Pellauer**, and Tushar Krishna*
ISCA 2018

## Slide 2: Acknowledgement (in particular for this session)
Mr. Charlie Hauck
Dr. Rishiyur Nikhil
Ananda Samajdar
Eric Qin
Yehowshua Immanuel
For providing BSV license for hands-on exercises
For ASIC and FPGA synthesis/PnR

## Slide 3: Outline
Tool Flow of MAERI
Design
Architecture
Source code and MAERI front-end
Demo
Hands-on Exercises

## Slide 4: Tool Flow of MAERI

## Slide 5: Bluespec System Verilog (BSV)
A high-level hardware description language
  Generates fully synthesizable Verilog
Inspired by Haskell and System Verilog
  Strong type-checking system and polymorphism
  System Verilog-like syntax
  Intuitive module interfaces
Based on “guarded atomic action” blocks
  Provides coarse-grained description of parallel actions
For details, please refer to “BSV by Example” (http://csg.csail.mit.edu/6.S078/6_S078_2012_www/resources/bsv_by_example.pdf)

## Slide 6: Outline
Tool Flow of MAERI
Design
Architecture
Source code and MAERI front-end
Demo
Hands-on Exercises

## Slide 7: Background: Convolutional Layer in CNN
Compute weighted sum
Independent multiplication
Accumulation of multiplication results
Notes: First show CNN sliding window figure

## Slide 8: Fully Flexible Accelerator
MultiplierPool
Adder
Pool
VN0
VN1
VN2
Virtual Neuron (VN): Temporary grouping of compute units for an output (neuron)
How to enable flexible grouping?
“MultAlloc(3); AddAlloc(2)”
Need to provide flexible connectivity among arbitrary compute units and buffer

## Slide 9: Practical Approach: Minimal Switches
2 x 2 switch
3 x 2 switch
One port for distribution
One port for local forwarding
Two ports for collection
Extra port for flexible mapping
Using these minimal switches...
How do we design a specialized connectivity (topology) allowing flexible mapping?

## Slide 10: Connectivity: Distribution of Weights/Inputs
Extra bandwidth
Features
Fat tree-based topology
  Supports multicasting for spatial data reuse
Extra bandwidth near the top
  Provides high bandwidth that enables multiple multicasting simultaneously

## Slide 11: Connectivity: Local Communication
Enables spatio-temporal date reuse

## Slide 12: Connectivity: Reduction/Collection of Outputs
Extra bandwidth
Extra link
Extra link
enabled
red VN
Augmented Reduction Tree (ART)
Features
Extra links
  Supports non-blocking in-network reductions for arbitrary virtual neuron sizes
  Provides high compute unit utilization
Extra bandwidth near the root switch
  Provides high bandwidth that enables multiple reduction (accumulation) simultaneously

## Slide 13: Outline
Tool Flow of MAERI
Design
Architecture
Source code and MAERI front-end
Demo
Hands-on Exercises

## Slide 14: Switch Microarchitecture
Light-weighted structure

## Slide 15: MAERI DNN Accelerator
(VN Construction)

## Slide 16: Regular and Irregular Dataflow
DNN Topologies
  Layer size / shape
  Layer types: Convolution / Pool / FC / LSTM
  New sub-structure: e.g., Inception in Googlenet
Compiler Optimization
  Loop reordering
  Loop tiling size
  Cross-layer mapping
Algorithmic Optimization
  Weight pruning: Sparse workload
Our Key insight: Each dataflow translates into neurons of different sizes

## Slide 17: Dense Dataflow

## Slide 18: Irregular Dataflow Support Example
Sparse Convolutional Layer

## Slide 19: Irregular Dataflow Support Example
Fully-connected / LSTM layer
Details in paper!
* H. Kwon et al., “MAERI: Enabling Flexible Dataflow Mapping over DNN Accelerators via Reconfigurable Interconnects,” ASPLOS 2018

## Slide 20: Outline
Tool Flow of MAERI
Design
Architecture
Source code and MAERI front-end
Demo
Hands-on Exercises

## Slide 21: Source code directory structure
maeri_code_isca2018_tutorial
src
scripts
ART
distribution_network
multiplier_switch
fixedPointUnits
types
lib
testbench
MAERI core implementation
Internal BSV type definitions
Custom libraries
Augmented reduction tree
Distribution tree
Multiplier switch and its array
Fixed point adder/multiplier
Testbenches

## Slide 22: How to use MAERI front-end
Configuration change
  Modify AcceleratorConfig.bsv at the top directory
    Distribution bandwidth
    Reduction bandwidth
    Number of multiplier switches
Verilog code generation and simulation
  ./Maeri –c : Compile a simulation
  ./Maeri –r : Run compiled simulation
  ./Maeri –w : Launch GTKwave for waveform analysis
  ./Maeri –v : Generate Verilog code
  ./Maeri –clean : Clean up intermediate files

## Slide 23: How to use MAERI front-end
Simulation results example
  Triggered with “./Maeri –r” after “./Maeri –c”

## Slide 24: How to use MAERI front-end
Waveform Analysis
  Triggered with “./Maeri –w” after “./Maeri –r”

## Slide 25: How to use MAERI front-end
Verilog generation example
  Triggered with “./Maeri –v”
* Verilog files are generated in “(Top_Directory)/Verilog”
Generated Verilog code is synthesizable!

## Slide 26: MAERI Synthesis/PnR
Synthesis/PnR Environment
  Technology: TSMC 28nm
  Clock frequency: 1GHz
  Design: 64 multiplier switches and 31 adder switches
  Distribution Bandwidth: 16/4/1 data per cycle
  Gather Bandwidth: 16/4/1 data per cycle
  RTL Code: Verilog generated using MAERI code base
  CAD Tool Chain: Synopsys Design compiler, Cadence Innovus, Primepower

## Slide 27: Post-layout Area and Power
Number of PEs | Distribution BW | Reduction BW | Area (mm2) | Power (mW)
64 | 16X | 4X | 0.440 | 407.861
64 | 4X | 16X | 0.255 | 252.326
64 | 4X | 1X | 0.219 | 194.912
64 | 1X | 4X | 0.239 | 254.603
* Based on 28nm technology and 1GHz clock

## Slide 28: Outline
Tool Flow of MAERI
Design
Architecture
Source code Structure
Using MAERI source code base
Demo
Hands-on Exercises

## Slide 29: Demo
Launching cycle-accurate simulations
Modifying user configuration
Compiling simulations
Launching wave form analysis
Generating Verilog files

## Slide 30: Outline
Tool Flow of MAERI
Design
Architecture
Source code Structure
Using MAERI source code base
Demo
Hands-on Exercises

## Slide 31: Revisiting Convention
K/C: Output/Input Channel
Y/X: Input activation height/width
R/S: Weight filter height/width

## Slide 32: Testbench Structure

## Slide 33: Testbench Dataflow (MAESTRO description)
  let sWindowSz = sizof(R) x sizeof(S)
  let numVNs = floor(NumMultSwitches / sWindowSz)
  Temporal_Map (1, 1) C
  Spatial_Map (1, 1) K
  Temporal_Map (1, 1) Y
  Temporal_Map(sWindowSz, 1) X
  Tile(sWindowSz)
  Unroll R
  Unroll S
High weight filter parallelism

## Slide 34
Exercise#1: Compile a simulation with default, early, and late layers with 32 PEs (“./Maeri –c,” “-/Maeri –ctarg EARLY_SYNTHETIC,” “./Maeri –ctarg LATE_SYNTHETIC”). Run simulation and compare results.
Exercise#2: Compile a simulation with 32 and 64 PEs using default seting (“./Maeri –c”). Run simulation and compare results
Exercise#3: Compile a simulation with 2X/4X/and 8X distribution bandwidth (fix reduction bandwidth as 4X). Run simulation and compare results.
Exercise#4: Compile a simulation with 2X/4X/and 8X reduction bandwidth (fix distribution bandwidth as 4X). Run simulation and compare results.
Notes: Simple exercises
1 Vary layers
2. Vary number of PEs (32/64)
3. NoC dist Bandwidth
4. NoC reduction Bandwidth